## Slide 1: Wamalloc: An Efficient Wear-Aware Allocator for Non-Volatile Memory
Jiashun Zhu, Sumin Li, Linpeng Huang
Department of Computer Science and Engineering
Shanghai Jiao Tong University

## Slide 2: Content
Background
Motivations
Design and implementation of Wamalloc
Evaluation
Conclusion
Notes: First I will talk about some necessary backgrounds about NVM and our motivations for a new memory allocator, we called it wamalloc, which stands for a wear-aware allocator.
Then, I will go deep into the design and implementation.
After that, I will show the performance and reach our conclusion.

## Slide 3: Content
Background
Motivations
Design and implementation of Wamalloc
Evaluation
Conclusion

## Slide 4: Emerging NVM Technology
  Comparable access speed as DRAM
  Byte addressability
  Key Features
PCM
STT-RAM
ReRAM
Notes: For decades, DRAM has been used as the main memory of computer system.
However, with the great demands of performance and energy-constrain applications, the defects of DRAM have become a main concern, for example, the limited density and its high energy consumption.
Fortunately, an emerging new technology named non-volatile memory provides the solution to address these problems.
NVM has the advantages of high density, low power consumption and byte-addressable, which make it a better alternative to be the main memory when compared with DRAM.
However, NVM suffers from limited write endurance.
For example, a typical PCM cell permanently fails after nearly ten to the power of seven to ten to the power of nine writes.
In such a situation, a poorly designed memory allocator will break NVM in a short time.
For purpose of tackling this problem and support a software level wear-aware memory allocator, a new memory allocator must be designed for applications running on NVM.

## Slide 5: NVM in Memory System
Notes: Due to the limitations, NVM is not likely to replace DRAM as the only main memory in computer system.
We assume that at least for write-intensive applications, a combination of DRAM and NVM should be used in computer systems, taking their respective advantages.
Here is the logical view of the hybrid memory system .

## Slide 6: Content
Background
Motivations
Design and implementation of Wamalloc
Evaluation
Conclusion

## Slide 7: Motivation for a New Allocator for NVM
Memory Allocators have been a key component of system software, making a significant impact on system performance
The unique features of emerging NVM bring new opportunities for Memory Allocators:
  Very high access speed
  Wear Leveling issues
There are a number of existing memory allocators for NVM, but they have limitations.
None of the current allocators can provide both an accurate wear-leveling policy and a good allocation performance simultaneously.
Notes: Memory Allocators have been a key component of system software, making a significant impact on system performance.
The unique features of emerging NVM bring new opportunities for Memory allocators.
It can provide very high access speed, which is a good property, however it suffers from wear-leveling problem.
There are a number of existing memory allocators for NVM, but they all have some kind of limitations!
We will compare them more deeply in the next slide.
None of the current allocators can provide both an accurate wear-leveling policy and a good allocation performance simultaneously.

## Slide 8: Motivation for a New In-Memory File System (Cont’)
Allocator | Allocation performance | Wear-leveling | Total Memory Usage
NVMalloc | 1(not fast enough) | Support(not good enough) | high
nvm_malloc | 2 | N/A | high
pmemalloc | 3 | N/A | high
Wamalloc | Expected to be the best | Expected to be the best | Expected to be the best
Larger number means poorer performance
Notes: The table shows the detail comparison between nowadays state-of-the-art nvm allocators.
We can see that NVMalloc is the best in these allocators, but our experiment shows that the overall performance and wear-leveling policy of NVMalloc is not good enough.
So it motivates us to write a better allocator.

## Slide 9: Content
Background
Motivations
Design and implementation of Wamalloc
Evaluation
Conclusion
Notes: Let’s go to the design part.

## Slide 10
Desgin Principles:
  Wear-leveling
  Low allocation latency
Design of Wamalloc
Overall structure
Notes: The most important design goal is wear-leveling.
Without hardware level wear-leveling, every time applications request memory, a memory block with the least allocation times so far is expected to be allocated.
However, a strict policy that allocates the exact block may introduce extra time penalty.
In later, we will see a hybrid method to tackle this problem.
Another requirement is low allocation latency, otherwise allocator would probably become the bottleneck of the entire application, which results in the allocator to be useless. To reduce the latency, every thread should have its own local heap to reduce the possible lock contention, and all memory owned by threads should be managed by a global heap.
The figure shows the overall structure of the system.
If a request from an application can be satisfied by its local heap, the allocation latency will be very low since there is no lock contention and no need to communicate with the global heap.

## Slide 11
Chunk is the basic unit that would be transferred between global heap and local heap
Chunk can be divided into several blocks base on its size class
Wamalloc uses two sets of size class: small-span(16B, 24B, 32B,..., 256B), large-span(384B, 512B,..., 32768B, 49152B, 65536B)
Chunk size has a fixed value to simply the design of global heap
Design of Wamalloc(Cont’)
Chunk Structure
Notes: Memory chunk is the basic unit that would be transferred between global heap and local heap, which consists of two parts: a small chunk header and a 64KB chunk body.
Chunk body is divided into several memory blocks based on its size class.
Obviously, with smaller size class comes more memory blocks.
Chunk header stores metadata such as the number of remaining free blocks, its size class and so on.
We uses two sets of size class: small-span and large-span.
For the memory requests larger than 64KB, it will be redirected to operating system via system call such as mmap.
In the beginning, all blocks are clean, which are indicated by a free pointer.
When a block is freed by the application, it is added to some kind of reuse list according to our wear-leveling policy to be discussed later.
Chunk size has a fixed value to simply the design of global heap.

## Slide 12: Local Heap
Local heap is maintained by each thread, which stores information to find the appropriate chunk
Every memory chunk in the local heap can be classified into five categories:
  in-use
  full
  waiting
  not-available
  clean
Notes: Local heap is maintained by each thread, which stores information to find the appropriate chunk.
Every memory chunk in the local heap can be classified into five categories:
in-use chunk means that when the application makes an allocation request, we will first find the appropriate size class, then use that size class find the current in-use memory chunk and allocate memory blocks from it.
After several memory requests of a particular size class, a memory chunk may be out of blocks, which is called a full chunk.
Chunks in a waiting list are called waiting chunks. Waiting chunks are the chunks in a partially allocated state. When a block in a full chunk is freed, it becomes to a waiting chunk.
Consider the things we discussed so far, a typical life cycle of a memory chunk could be first used as in-use chunk, then full chunk, then waiting chunk, and back and forth repeatedly. For the wear-aware purpose, that is not what we expect.
Thus we add a wear-aware variable to each memory chunk and define an allocation threshold.
When a chunk is first allocated from global heap, its wear-aware variable is set to zero.
Every time a block is allocated from a chunk, the variable increases by one.
If the variable reaches the predefined allocation threshold, it is no longer available for allocation in this thread, and its state becomes to not-available.
When all the blocks in a not-available chunk are freed, the chunk will be returned back to global heap.
Finally, a Clean chunk means a chunk without a specific size class.
The figure shows how the state of a chunk is changed.

## Slide 13: Local Heap Structure
Notes: Here is the structure of a local heap, which is maintained by every thread.
We can find the appropriate chunk according to size class.

## Slide 14: Global Heap
Global heap maintains the whole memory chunks obtained from operating system.
Global heap structure
Notes: Global heap maintains the whole memory chunks obtained from operating system.
In the beginning, all the chunks are clean, indicated by a free pointer.
After a chunk is returned to global heap, it will be added to some kind of pools related to our wear-leveling policy

## Slide 15: Design of Wamalloc(Cont’)
Use different wear-leveling policy in different level:
  In block level: FIFO queue is enough
  In local heap level:
    FIFO queue is enough
    Use waiting chunk first, then clean chunk
    Add a wear-aware count, if reaches threshold, then not available, ready to return to global heal
  In global heap level :
    A minheap is used to implement the priority queue to find the chunk of the minimum allocation time.
    Chunks are not moved to global pool synchronously, instead, the real action is taken under the ground asynchronously
Notes: Now let’s discuss the wear-leveling policy in different level in detail.
The overall purpose is quite simple: all memory blocks are expected to be allocated evenly.
In block level, it is obviously that memory block starting from the free pointer should be allocated first because these memory blocks have never been allocated since this chunk is assigned to its local heap.
After a chunk runs out of these blocks, a free list will be checked to find out whether any reusable block is available.
In consideration of allocation latency, a simple and fast method is more appropriate in this situation.
Thus, we consider the free list as a FIFO queue.
In local heap level , When the current in-use chunk runs out of blocks, a chunk should be chosen as a new in- use chunk.
Since Clean chunks don’t belong to any size class, they are more flexible than the chunks in waiting chunk list, so we will choose waiting chunks first.
With the wear-aware variable to ensure the upper bound of allocation times, We think FIFO is still our best choice in this level.
In global heap level, when the clean chunk is running out, the best wear-leveling policy should return the least allocated chunks so far, so our optimized minimum heap is used to find the chunk of the minimum allocation times.
What’s more, Chunks are not moved to global heap synchronously, instead, the real action is taken under the ground.

## Slide 16: Allocation/Deallocation Algorithm of Wamalloc
Allocation:
  use size get the size class, then use the size class find the current in-use chunk to allocate block
  if full, then look for a waiting/clean chunk
  otherwise ask for chunk from global heap
Deallocation:
  put the memory block into per-chunk list
  If full, then waiting
  If clean, then move the chunk to clean list
Notes: This is the allocation and deallocation algorithm.
When an allocation happens, the parameter size passed by user is used to get the size class, then this size class is used to find out the current in-use chunk.
If it is a full chunk, then look for a waiting or clean chunk, otherwise ask for chunk from global heap.
When a deallocation happens, wamlloc just put the memory block into a per-chunk FIFO queue.
If the chunk is full before deallocation, then it becomes to a waiting chunk.
If the chunk is clean after deallocation, it becomes to a clean chunk.

## Slide 17: Pseudocode of Wamalloc
Notes: Here is the pseudocode, the procedure we have just discussed.

## Slide 18: Content
Background
Motivations
Design and implementation of Wamalloc
Evaluation
Conclusion

## Slide 19: Evaluation
We have implemented Wamalloc and evaluated its performance on:
  wear-leveling against NVMalloc
  total memory usage against NVMalloc
  allocation performance against NVMalloc and glibc
Notes: We have implemented Wamalloc and evaluated its performance on wear-leveling, total memory usage and allocation performance against NVMalloc.
When we evaluate allocation performance, we also add glibc into comparison to give a baseline.

## Slide 20: wear-leveling
Wamalloc outperforms other memory allocators
Notes: First, we evaluate the ability of wear-leveling using a test program under uniform and random allocation and deallocation operations.
These two Figures show the result in terms of average allocation frequency per block under uniform and random allocation.
Since Wamalloc uses a more elaborate and accurate wear-leveling policy than NVMalloc, it is expected that Wamalloc performs better than NVMalloc.

## Slide 21: total memory usage
Wamalloc outperforms other memory allocators
Notes: However, it is meaningless to compare the average allocation frequency without considering the physical memory consumption.
A simple allocator that allocates every memory block just once and never use that memory again could make this value to be one, while at the meantime it consumes plenty of physical memory, causing it to be a useless allocator.
Thus, next we are also supposed to measure the memory consumption of above evaluations under uniform and random allocation.
Evaluation shows that Wamalloc is more economic in physical memory usage than NVMalloc.

## Slide 22: allocation performance
Wamalloc outperforms other memory allocators
Notes: we also evaluate the average allocation latency as the number of parallel threads increases under the workload of uniform and random allocation.
From the result we can verify that Wamalloc outperforms both glibc and NVMalloc under different workloads.

## Slide 23: Content
Background
Motivations
Design and implementation of Wamalloc
Evaluation
Conclusion

## Slide 24: Conclusion
We observe the fact that no NVM allocators at the time of writing can provide both an accurate wear-leveling policy and a good allocation performance simultaneously.
Based on the observation, we propose an efficient wear-aware NVM allocator, Wamalloc, which uses a thread-cache memory architecture causing nearly no lock contention in critical path, and an elaborate hybrid wear-leveling policy to improve the lifetime of NVM.
The experimental results show that Wamalloc outperforms NVMalloc in different aspects.
Notes: Here is the conlusion.

## Slide 25: Thank you
Q & A